## Slide 1: Amphidrome ®

## Slide 2: Amphidrome® System Benefits
Highest Level of Nitrogen Removal of any system available
Low Visual Impact
Small Foot Print
Media is submerged in liquid - nitrification reaction unaffected by air temperature
All effluent filtered through deep sand bed

## Slide 3: Amphidrome® Process
Biological Nutrient Removal (BNR) Process
  TSS
  BOD5
  Total Nitrogen
  Oil and grease
One reactor
  BAF Biologically Active Filter
  Functions as a Submerged Attached Growth Bioreactor (SAGB) operating in sequencing batch mode

## Slide 4: SAGB
Media is submerged in liquid acting as both growth media and filter.
Fine media provides higher concentration of biological growth for enhanced loading capacity.
Media acts as a physical filter
  low effluent TSS.
Underground reactor and submerged media performs well in cold weather

## Slide 5: Process Description
Main reactor designed to achieve
  BOD5 and nitrogen removal
  solids separation
Intermittent aeration
Plus reactor
  Enhanced denitrification
  Phosphorus removal by chemical addition and filtration (optional)

## Slide 6: Process Description
Batch is cycled through the reactor
Treatment varies between aerobic to anoxic
Nitrification and denitrification in a single reactor

## Slide 7: Anoxic/Equalization Tank
Solids settling
Sludge storage
Secondary functions
  Buffers the dissolved oxygen in the recycled flow
  Mixes recycle with influent organic carbon to promote de-nitrification

## Slide 8: Main Reactor Function
Media provides surface area for biofilm growth
Provides solids separation eliminating the need for downstream clarification
Intermittent aeration
  typical 3 minutes on 15 minutes off

## Slide 9: REACTOR UNDER AERATION

## Slide 10: REACTOR IN “AIR OFF” MODE

## Slide 11: Clearwell Function
Stores batch volume
Stores some fraction of backwash volume
Contains backwash and effluent pumps

## Slide 12: Amphidrome™plus
Polishing denitrification filter

## Slide 13: Installation

## Slide 14: Controls
OPERATOR INTERFACE
AND
CONTROL

## Slide 15: Main Touch Screen Display
Indicates current operation status of various equipment.
Provides access to individual component screens.
  Simply touch on the item you wish to see.

## Slide 16: Component Screen Display
Component status screen shows the status of specific equipment.
Provides access to control screens.
Component process controls easily accessed.
On-screen help.

## Slide 17: Component Screen Display

## Slide 18
Troubleshooting Screen

## Slide 19: Aeration Control
Process Air - air required for oxidation of organics and ammonia
  Adjusts automatically to flow
  Operator is only has to be concerned with one adjustment, the Aeration Factor (AF)

## Slide 20: Process Air Control Screen

## Slide 21: Remote Access
Remote Access and Control
  Web access to plant via the internet
  Remote monitoring of system
  Remote Control of system
  Access to touch screen as if standing in front of it.

## Slide 22
Remote Access